## Slide 1: Linear Time Invariant Systems as Frequency-Selective Filters (Unit 3)

## Slide 2
The desired filter characteristics are specified in the frequency domain - desired magnitude and phase response of the filter
In the filter design process, we determine the coefficients of a causal FIR or IIR filter that closely approximates the desired frequency response specifications.
The issue of which type of filter to design, FIR or IIR, depends on the nature of the problem and on the specifications of the desired frequency response.
Filter Design Flow

## Slide 3
In general, a linear time-invariant system modifies the input signal spectrum X(ω) according to its frequency response H(ω) to yield an output signal with spectrum
Y(ω) = H(ω)X(ω)
H(ω) act as a spectral shaping function to the different frequency components in the input signal
Any linear time-invariant system can be considered to be a frequency-shaping filter
Consequently , the terms “ linear time-invariant system ” and “filter” are synonymous and are often used interchangeably

## Slide 4
The term filter is used to describe a linear time-invariant system that perform spectral shaping or frequency-selective filtering
Filtering is used in digital signal processing in a variety of ways,
removal of undesirable noise from desired signals,
spectral shaping such as equalization of communication channels,
signal detection in radar, sonar, and communications,
spectral analysis of signals

## Slide 5
Filters are usually classified according to their frequency-domain characteristics as
  Low pass
  Highpass
  Bandpass
  Band stop or band -elimination filters.
Ideal filters have a constant-gain (usually taken as unity-gain) passband characteristic and zero gain in their stopband.

## Slide 6: The ideal magnitude response characteristics of these types of filters are illustrated in Fig
Ideal filters have
a constant-gain passband characteristic
zero gain in their stopband

## Slide 7: Ideal filters have a constant-gain (usually taken as unity-gain) passband characteristic and zero gain in their stopband.

## Slide 8: Another characteristic of an ideal filter is a linear phase response
Assume that a signal sequence x(n) with frequency components confined to the frequency range is passed through a filter with frequency response, where C and α are constants
The signal at the output of the filter has a spectrum,
) = X) H)
= X)
By applying the scaling and time shifting properties of the fourier transform, the time domain output

## Slide 10: In conclusion,
Ideal filters have a constant magnitude characteristic and a linear phase characteristic within their passband.

## Slide 11: Causal LTI Systems Review (one slide)

## Slide 12: Causal LTI Systems - Review

## Slide 13: Ideal filters are not physically realizable but serve as a mathematical idealization of practical filters.
Eg. The ideal low pass filter impulse response,
This filter is not causal
it is not absolutely summable
it is also unstable.
Consequently, this ideal filter is NOT CAUSAL and hence it is physically unrealizable.

## Slide 14: Linear Phase FIR filters (FIR-finite impulse response filters)
Transfer function of a FIR causal filter H(z)
h(n) is the impulse response of the filter
The Fourier transform of h[n]

## Slide 15
Phase delay and group delay of a filter as
For FIR filters with linear phase,
phase delay and group delay will be constant and equal to delay ’

## Slide 16
Separating the real and imaginary part and taking the ratio is given below,

## Slide 17
Solving the above equation gives,
The above condition satisfies when,
and

## Slide 18: eg. For N =7 (odd) and N = 6 (even)
Implies h(n) is symmetric in nature
In general, considering symmetric and antisymmetric impulse response
FIR filter has linear phase if its unit impulse response satisfies the condition
h(n) =

## Slide 19: Generalized frequency response Expression for N odd and N even (Symmetric impulse response)

## Slide 20: Design of FIR filters using Windows

## Slide 21: Filter Design by Windowing
Simplest way of designing FIR filters
Start with ideal frequency response
Choose ideal frequency response as desired response
Ideal impulse responses are of infinite length [-]

## Slide 22
Possible way to obtain a causal FIR filter from ideal is
Disadvantage of abrupt truncation: Oscillations in stopband and passband, this effect is known as Gibbs phenomenon
To reduce these oscillations, the filter coefficients are modified by multiplying the infinite impulse response with a finite weighing w[n]
i.e., window function

## Slide 23
After multiplying with the window function, we get a finite duration sequence h(n)
It is instructive to consider the effect of the window function on the desired frequency response
Recall that multiplication of the window function w(n) with hd(n) is equivalent to convolution of Hd(ω) with W(ω)

## Slide 24
Fourier transform of window function W(ω) (Rectangular window)

## Slide 25
Fourier transform of w[n], W(ω)
w[n] is the rectangular window, with M samples, where M = N

## Slide 27
Specifically, the convolution of Hd(ω) with W(ω) has the effect of smoothing
As N increases, the main lobe of W(ω) becomes narrower.
  However, the sidelobes are relatively high and remain unaffected by an increase in N .
  Smoothing provided by W(ω) is reduced.
On the other hand, the large sidelobes of W(ω) result in some undesirable ringing effects in the FIR filter frequency response H(ω) and also in relatively larger sidelobes in H(ω)
The width of the main lobe is 4π/N )
N = M

## Slide 28
Rectangular window spectrum for N=25 samples

## Slide 29
Frequency response of Low pass filter at N=25

## Slide 30: Rectangular window spectrum for N=51 samples

## Slide 31: Undesirable ringing effect in FIR filter frequency response – Rectangular window, How it is overcome?
Best alleviated by the use of windows that do not contain abrupt discontinuities in their time-domain characteristics, and have correspondingly low sidelobes in their frequency-domain characteristics.

## Slide 32: Hanning Window
Hanning window - time domain
Hanning window - frequency domain - N=25

## Slide 33
Hanning window - frequency domain – N=51

## Slide 34: Hamming window
Hamming window: Time domain
Hamming window: Frequency domain

## Slide 35
Hamming window: Frequency domain

## Slide 36
Frequency response of LPF using Hamming window

## Slide 37
Other window functions

## Slide 38: Exercise

## Slide 41
(Mathematical expressions)
Other window functions

## Slide 43
The above filter designed has to be linear phase also.

## Slide 63: Assignment
Digital Differentiator
Hilbert Transformer
Real life applications of Signal Processing (Minimum 2 Scenarios)

## Slide 64: IIR Filter Design
In the design of frequency-selective filters, the desired filter characteristics are specified in the frequency domain in terms of the desired magnitude and phase response of the filter.
In the filter design process, we determine the coefficients of a causal FIR or IIR filter that closely approximates the desired frequency response specifications.
The issue of which type of filter to design, FIR or IIR, depends on the nature of the problem and on the specifications of the desired frequency response.

## Slide 65
In practice, FIR filters are employed in filtering problems where there is a requirement for a linear-phase characteristic within the passband of the filter.
If there is no requirement for a linear-phase characteristic, either an IIR or an FIR filter may be employed. However, as a general rule, an IIR filter has lower sidelobes in the stopband than an FIR filter having the same number of parameters.
  For this reason, if some phase distortion is either tolerable or unimportant, an IIR filter is preferable, primarily because its implementation involves fewer parameters, requires less memory and has lower computational complexity.

## Slide 66
Digital IIR filter design - based on converting an analog filter into a digital filter
Analog filter design is a mature and well developed field
Begin the design of a digital filter in the analog domain and then convert the design into the digital domain.

## Slide 67
An analog filter can be described by its system function.

## Slide 68
Analog linear time invariant system is stable if all its poles lie in the
left half of s plane

## Slide 69
Keywords:
ROC -
Region of Convergence
Re(s) = σ
Im(s) = Ω

## Slide 72
Keywords:
ROC -
Region of Convergence,
Unit Circle

## Slide 76: Design of Digital filters from Analog filters
For the given specifications of a digital filter,
Map the desired digital filter specifications into those for an analog filter
Derive the analog transfer function for the analog protype
Transform the transfer function of the analog prototype into an equivalent digital filter transfer function
Transformation methods:
  Bilinear transformation
  Impulse Invariant Transformation

## Slide 77
Magnitude response of LPF: Digital filter
Pass band error tolerance
Maximum allowable magnitude in stopband

## Slide 78: Analog Lowpass filter design
An analog filter can be described by its system function
For a stable analog filter, the poles of H(s) lie in the left half of s- plane
Two types of Analog filter design:
Butterworth filter
Chebyshev filter

## Slide 79
Butterworth filter
Low pass Butterworth magnitude response
N is the order of the filter
is the cut off frequency
Maximum response at frequency = 0
Ideal response shown in dash line
Magnitude response approaches ideal as N increases
For frequency less than cut off frequency, magnitude approximately equal to 1
At frequency = cut off frequency, the curve passes 0.707 or -3dB

## Slide 81
Magnitude squared function of Normalized Butterworth filter (Cutoff frequency = 1 rad/sec)
To derive the transfer function of a stable filter
Omega= s/j
(s/j)^2

## Slide 82: Implications
Poles lies in both left half and right half of s plane (H(s) & H(-s))
If H(s) has roots in one half implies H(-s) in other half of s plane
Obtain the roots by equating the denominator to zero
N odd,
the roots as shown
N even,
the roots as shown

## Slide 83
N =3, implies
Pole locations in the s plane
To ensure stability, only left half poles is considered.

## Slide 84
N=3;
To ensure stability, only left half poles is considered.
So, the transfer function of third order Butterworth filter for unity cut off frequency 1 rad/sec is ,
i.e.,
Transfer function of unnormalized transfer function is obtained
by substituting ‘s’ as ‘s/cut off frequency ‘

## Slide 85: List of Butterworth polynomials

## Slide 86
How to determine the order, given the filter speciifcations
Maximum passband attenuation at passband
edge frequency
Maximum stopband attenuation at stopband
edge frequency
Taking logarithm on both sides,

## Slide 87
Similarly, considering stopband attenuation,
After simplification,

## Slide 88
Order of filter
Since N does not result in integer, we roundoff to the next
higher integer
Where

## Slide 89
Cut off frequency
Eqn. (2)
Eqn. (1)
Comparing 1 and 2 , we get the expression for cut off frequency
How to derive the expression for cut off frequency?

## Slide 90: Design steps for analog Butterworth Filter
N

## Slide 91
therefore, N = 4
=
Normalized Butterworth filter for N = 4

## Slide 93: Transformation (H(s) H(z))
Impulse Invariant Transformation
Bilinear Transformation

## Slide 94: Impulse Invariant Transformation
IIR digital filter is designed such that unit impulse response h(n) of digital filter is the sampled version of analog filter.
Let H (s) is the system function (Transfer function) of analog filter.
The inverse laplace transform

## Slide 95
Sample this analog signal at t = nT, where T is the sampling period

## Slide 96: Steps to design a filter using Impulse Invariant method

## Slide 97
Impulse Invariant Transformation

## Slide 98: Impulse Invariant Transformation (Underlying mapping function)
The mapping is characterized by
Implies, and

## Slide 99: Pole on jΩ axis (σ= 0)

## Slide 100: Pole in the left half of s-plane (σ <0)

## Slide 101: Pole in the right half of s-plane (σ >0)

## Slide 102: Disadvantages of Impulse Invariant
Many to one mapping
Illustration: Analog poles at

## Slide 103
S1 pole

## Slide 104
To remember
Transform H(s) to H(z)

## Slide 105: Bi-Linear Transformation

## Slide 109
Relation between analog and discrete frequency in Bi-linear Transformation

## Slide 110
For low frequencies, relationship between analog and discrete frequencies are linear
For high frequencies, relationship between analog and discrete frequencies become non linear, due to this distortion is introduced in the frequency scale of digital filter – WARPING EFFECT

## Slide 111
The warping effect can be eliminated by pre-warping the analog filter
-

## Slide 112: Steps to design using Bilinear transformation
From the given specifications, find the prewarped frequencies
Using the analog frequencies, find H(s) of the analog filter
Select the sampling rate T
Substitute,

## Slide 113: Design a digital Butterworth filter with T = 1 sec (sampling period) using Bilinear transformation