## Slide 1: UNIT I - Electrostatics, Magnetostatics and Electrodynamics
Electric & Magnetic (EM) fields and forces are the basis of modern electrical systems
EM represents an essential and fundamental background that underlies future advances in energy systems
Understanding of electric fields is important for understanding the operating principles of many semiconductor and nanotechnology devices such as Computer chip Design and circuits
Lightning is an electrostatic discharge that travels between two charged regions.

## Slide 2
ELECTRIC FIELDS
Objective
To define electric field by means of electric field lines
To calculate electric field due to
  Point Charge
  continuous charge distributions using Coulomb’s law

## Slide 3
Electric Field
Electric field is said to exist in the region of space around a charged object: the source charge.
Concept of test charge:
  Small and positive
  Presence of test charge is not necessary for the field to exist;
  Does not affect charge distribution on the charge object
    Thus the test charge does not alter the electric field we are defining.
Existence of an electric field is a property of its source
The electric field at point P (Fig. 1a) is
  The magnitude of the electric field at point P (Fig. 1) is
  E = F/q0
Fig. 1: (a) The electrostatic force acting on a positive test charge near a sphere of uniform negative charge.

## Slide 4
To visualize electric fields
Michael Faraday, who introduced the idea of electric fields in the 19th century, thought of the space around a charged body as filled with lines of force.
Electric field lines, provide a nice way to visualize patterns in electric fields (Fig. 1b)
Relation between the field lines and electric field vectors:
The direction of the tangent to a curved field line gives the direction of at that point, and
The field lines are drawn so that the number of lines per unit area, measured in a plane that is perpendicular to the lines, is proportional to the magnitude of .
If E is large, the field lines are close together
If E is small, the lines are far apart
Fig. 1b: The electric field vector at the location of the test charge, and the electric field lines in the space near the sphere.
The field lines extend toward the negatively charged sphere. (They originate on distant positive charges.)

## Slide 5
Net electrostatic force acting on the test charge would be perpendicular to the sheet, because forces acting in all other directions would cancel one another as a result of the symmetry.
Net force on the test charge would point away from the sheet
Electrostatic force , electric field vector and electric field lines of an infinitely large, nonconducting sheet
with uniformly distributed positive charge on one side
at any point in the space on either side of the sheet is also perpendicular to the sheet and directed away from it
The field lines extend away from the positively charged sheet.
Charge is uniformly distributed along the sheet, all the field vectors have the same magnitude. (uniform electric field)
(c) Side view of (b)
(b)
(a)

## Slide 6
Field lines for two equal positive point charges.
Field lines for two equal positive charges
The pattern of field lines and the electric field it represents have rotational symmetry about an axis passing through both charges in the plane of the page.
is tangent to the field line through the point.
Field lines for a positive point charge and a nearby negative point charge that are equal in magnitude.

## Slide 7
To find the Electric Field Due to a Point Charge (Positively charged)
Put a positive test charge q0 at that point as shown in Fig 2.
  From Coulomb’s law, the electrostatic force acting on q0 is
The direction of is the same as that of the force on the positive test charge
  directly away from the point charge if q is positive, and toward it if q is negative.
Net (or resultant), electric field due to more than one point charge
Placing positive test charge q0 near n point charges q1, q2,..., qn;
Net force from the n point charges acting on the test charge is
This shows that the principle of superposition applies to electric fields as well as to electrostatic forces.
Fig 2

## Slide 9
Calculating From Coulomb’s Law
Fig.3 shows an element of charge dq = r dV that is small enough to be considered a point charge.
Coulomb’s law gives the electric field at a field point P due to this element of charge as:
where is a unit vector that points from the source point to the field point P.
The total field at P is found by integrating this expression over the entire charge distribution. That is,
where dq = r dV
If the charge is distributed on a surface, we use dq =s dA
For charge distributed on a line, we use dq =l dL
and integrate over the surface or line.
Fig.3

## Slide 10
Step 1: Divide the ring into differential elements of charge that are so small that they are like point charges, and hence the equation below can be applied.
Step 2: Add the electric fields set up at P by all the differential elements. The vector sum of the fields gives us the field set up at P by the ring
A ring of uniform positive charge.
A differential element of charge occupies a length ds (greatly exaggerated for clarity).
This element sets up an electric field at point P.
The perpendicular components just cancel but the parallel components add.
Fig. 4 shows a thin ring of radius R with a uniform positive linear charge density l around its circumference.
Assume the ring to be made of plastic or some other insulator, so that the charges can be regarded as fixed in place.
on the Axis of a Ring Charge
To Find on the Axis of a Ring Charge
Let ds be the (arc) length of any differential element of the ring.
Since l is the charge per unit (arc) length, the element has a charge of magnitude dq = l ds.
dq sets up a differential electric field at point P

## Slide 11
Fig.4 shows that at point P is at angle  to the central axis (which we have taken to be a z axis) and has components perpendicular to and parallel to that axis
The perpendicular components just cancel but the parallel components add.
Every charge element in the ring sets up a differential field at P, with magnitude given by
have identical parallel (dE|| = dE cos  ) and perpendicular (dE = dE sin  )components; in both magnitude and direction.
dE directed perpendicular to the axis and it cancel in pairs (see Fig. 4)
From the symmetry of the charge distribution, we can see that the net field due to the entire ring must lie along the axis of the ring; that is, the perpendicular components sum to zero.
Magnitude of E due to the Parallel component along the axis of the ring is
q: the total charge on the ring = l(2pR)
Hence
on the Axis of a Ring Charge

## Slide 12
Z >> R; the ring “looks like” a point charge. Hence we have
For a point at the center of the ring — that is, for z = 0; E = 0
This is because if we were to place a test charge at the center of the ring, there would be no net electrostatic force acting on it; the force due to any element of the ring would be canceled by the force due to the element on the opposite side of the ring.