## Slide 1: JFET characteristics

## Slide 2: Two main characteristics
Transfer characteristics
Output characteristics

## Slide 3: Output characteristics - comparison
CE transistor characteristics
JFET characteristics
For different
IB is acting as controlling current
For different (controlling voltage)
For n channel JFET
<0
For n channel JFET
0

## Slide 4
If VGS is more and more negative, reverse bias happens on P type material
The pinch off can achieve at lower value of VDS

## Slide 5
Ohmic region
The VDS and ID are linearly related
Saturation region
After pinch off, the ID reaches to a saturation level,. This value decreases as the VGS become more and more negative
Cut off region
When VGS=-VP, then the ID=0 and the device will off completely

## Slide 6: Transfer characteristics

## Slide 7: Transfer characteristics
Draw a horizontal line from the output characteristics to the transfer characteristics graph and mark ID in it
Draw a vertical line from the VGS value and join on corresponding ID
Then we will get transfer characteristics plot
A non linear graph

## Slide 8: Comparison of output current of BJT and JFET
When VGS=0, ID=IDSS
When VGS=VP, ID=0

## Slide 9: Thank You