## Slide 1: Lecture 11 Nodal Analysis

## Slide 2: Introduction
Nodal analysis is a procedure for analyzing circuits.
This procedure utilizes node voltages as circuit variables.

## Slide 3: Node ????
Node
Node
Node
A Node is the point of connection between two or more branches

## Slide 4: Circuit with current source
The figure shows a circuit with two current sources I1 and I2. The circuit also consists of 3 resistors R1, R2 and R3.

## Slide 5: Nodes
There are 3 nodes in the circuit
Node 0, Node 1, Node 2
Lecture 11

## Slide 6: Reference Node
Node 0 is considered as reference node
Lecture 11

## Slide 7: Non reference Nodes
Node 1 and Node 2 are considered to be non reference nodes
Lecture 11

## Slide 8: voltage at Non Reference Nodes
v1 and v2 are voltages at nodes 1 and 2 respectively
Lecture 11

## Slide 9: Current flow in a resistor
i = (vhigher − vlower)/R
i1 = (v1 − 0)/R1
i2 = (v1 − v2)/R2
i3 = (v2 − 0)/R3
Lecture 11

## Slide 10: Application of K. C. L. at Node 1
Applying K. C. L. at node 1: I1= i1+ i2 +I2 --(1)
Lecture 11

## Slide 11
I1= i1+ i2 + I2------(1)
I1- I2= (v1 − 0)/R1+ (v1 − v2)/R2
----------------- (2)
i1 = (v1 − 0)/R1
i2 = (v1 − v2)/R2
i3 = (v2 − 0)/R3
Lecture 11

## Slide 12: Application of K. C. L. at Node 2
Applying K. C. L. at node 2: I2 + i2= i3 ------ (3)
i1 = (v1 − 0)/R1
i2 = (v1 − v2)/R2
i3 = (v2 − 0)/R3
I2+(v1 − v2)/R2= (v2 − 0)/R3--------------(4)
Lecture 11

## Slide 13
I1- I2= (v1 − 0)/R1+ (v1 − v2)/R2
  ------------- (2)
I2+(v1 − v2)/R2= (v2 − 0)/R3 --------------(4)
On solving (2) and (4) v1 and v2 is calculated. Once v1 and v2 is calculated current flowing through all resistances can be calculated.
Lecture 11

## Slide 14: Calculate the current In R1, R2 and R3 in the circuit shown in figure
I1 = 4A
I2 = 6A
R1=10Ω
R2=5 Ω
R3=20 Ω
The value of the resistances is given
Lecture 11

## Slide 15
I1- I2 = (v1 − 0)/R1+ (v1 − v2)/R2-------- (2)
Equation (2)( Node1 equation)
I2+(v1 − v2)/R2= (v2 − 0)/R3 --------------(4)
Equation (4)(Node2 equation
I1 = 4A
I2 = 6A
R1=10Ω
R2=5 Ω
R3=20 Ω
Lecture 11

## Slide 16
I1- I2 = (v1 − 0)/R1+ (v1 − v2)/R2
  ------------- (2)
I2+(v1 − v2)/R2= (v2 − 0)/R3 --------------(4)
I1 = 4A
I2 = 6A
R1=10Ω
R2=5 Ω
R3=20 Ω
4-6= (v1 − 0)/10+ (v1 − v2)/5
  ------------- (2)
-2= v1 /10+ (v1 − v2)/5------(5)
Lecture 11

## Slide 17: From previous slide equation(5) is obtained for Node 1
-2= v1 /10+ (v1 − v2)/5------(5)
Multiply (5) by 10
-20= v1+ 2*(v1 − v2)
-20= v1+ 2*v1−2*v2
3*v1−2*v2= -20--------------(6)
I1 = 4A
I2 = 6A
R1=10Ω
R2=5 Ω
R3=20 Ω
Lecture 11

## Slide 18
3*v1−2*v2= -20--------------(6)
At Node 2 from equation (4)
I2+(v1 − v2)/R2= (v2 − 0)/R3 ---------(4)
6+(v1 − v2)/5= (v2)/20 ----------------(7)
Multiply (7) by 20
120+4*v1 − 4*v2= v2
-4*v1+ 5*v2=120-----------------(8)
Solving (6) and (8)
v1 = 140/7= 20v
Sub v1 in equation (6)
3*(20)−2*v2= -20--------------(6)
v2=(80/2)=40V
Lecture 11

## Slide 19
v1 = 20v
v2=40V
i1 = (v1 − 0)/R1
i2 = (v1 − v2)/R2
i3 = (v2 − 0)/R3
R1=10Ω
R2=5 Ω
R3=20 Ω
i1= (20-0)/10=2A
i2=((20-40)/5)=-4A(negative sign indicate current direction is opposite to assumed direction of current.
i3=((40-0)/20)=2A
Lecture 11

## Slide 20
Thank You