## Slide 1
Lecture 12 Nodal Analysis

## Slide 2
Introduction
Analyse the circuit shown in figure and calculate v0.
2
Lecture 12

## Slide 3
Circuit with Voltage source
3
The Node ‘0’ is considered as reference Node.
V0 is the voltage at node 1.
Application of K. C. L. is required.
Lecture 12

## Slide 4
Calculation of Nodal voltage
4
I1+I2=I3------------(1)
((30-v1)/2kΩ)+((20-v1)/5kΩ)=(v1/4kΩ)
(30/2kΩ)-(v1/2Ω)+(20/5kΩ)-(v1/5kΩ)=(v1/4kΩ)
------------(2)
Equation (2)*20KΩ
10*30-10*v1+4*20-4*v1=5*v1
v1=20V=v0
I1= (30-v1)/2kΩ)
I2= (20-v1)/5kΩ)
I3= (v1/4kΩ)
Lecture 12

## Slide 5
Analyze the circuit and calculate V1 and V2 using Nodal analysis
5
Lecture 12

## Slide 6
Currents in each connection to each Node
6
At Node 1 applying K. C. L.
(4-v1)/5=(v1-v2)/10+(v1/15) ----------- (1)
Multiply equation (1) by 30
24 − 6v1 = 3v1 − 3v2 + 2v1------------ (2)
Lecture 12

## Slide 7
Current flow in a resistor
Lecture 1
7
11v1 − 3v2 = 24 ---------------(3)
At node 2
(v1-v2)/10 =(v2-6)/12+v2/8 --(4)
Lecture 12

## Slide 8
Application of K. C. L. at Node 2
Lecture 1
8
At node 2
(v1-v2)/10 =(v2-6)/12+v2/8 --(4)
Multiply (4) by 120
12v1 − 12v2 = 10v2 − 60 + 15v2 ----- (5)
Lecture 12

## Slide 9
Lecture 1
9
12v1 − 37v2 = −60 ------ (6)
11v1 − 3v2 = 24 ---------(3) on solving
v2 = 2.55 V
v1 = 2.88 V
Lecture 12

## Slide 10
Thank You
10
Lecture 12