## Slide 1: Lecture 15 Magnetic Circuits

## Slide 2: Magnetism
A coil of wire carrying an electric current can be used to magnetise a piece of iron or steel – Property is Magnetism
Magnetic lines of force – Magnetic flux
Magnetic field
I

## Slide 3: Magnetic Effects of Electric Current
A conductor carrying an electric current will be surrounded by a magnetic field
A conductor may be wound into a coil to increase the strength of the magnetic field
An iron core placed inside the coil will greatly increase the strength magnetic field

## Slide 4
Electromagnets:
Principle: An electric current flowing in a conductor creates a magnetic field around it.
Strength of the field is proportional to the amount of current in the coil.
The field disappears when the current is turned off.
A simple electromagnet consists of a coil of insulated wire wrapped around an iron core.
Widely used as components of motors, generators, relays etc.
N
I
Magnetic Effects of Electric Current

## Slide 5: Magnetic circuit
The complete closed path followed by any group of magnetic lines of flux
Equivalent electrical circuit

## Slide 6
Magneto Motive Force, MMF (F)
  Force which drives the magnetic lines of force through a magnetic circuit
  MMF, F = ΦS, where ‘Φ’ is the magnetic flux and ‘S’ is the Reluctance of the magnetic path.
  Also, For Electromagnets:
  where N is the number of turns of the coil and I is the current flowing in the coil
    Unit: AT (Ampere Turns)
  Basic Definitions
Analogy: EMF, V=IR
MMF= N I (No. of turns*Current),

## Slide 7: Magnetic flux (Φ):
  Basic Definitions
  Number of magnetic lines of force created in a magnetic circuit.
  Unit : Weber (Wb)
Analogy: Electric Current, I

## Slide 8: Reluctance [S]
  Opposition of a magnetic circuit to the setting up of magnetic flux in it.
  S=F/ɸ
  Unit: AT / Wb
  Basic Definitions
Analogy: Resistance

## Slide 9
  No. of magnetic lines of force created in a magnetic circuit per unit area normal to the direction of flux lines
  B = Φ/A
  Unit : Weber/m2 (Tesla)
Magnetic Field Strength (H)
  Basic Definitions
  The magneto motive force per meter length of the magnetic circuit
  H = (N I) / l
  Unit : AT / meter
Magnetic Flux Density (B):
Analogy: Current Density
Analogy: Electric field strength

## Slide 10
  Basic Definitions
Permeability (µ)
A property of a magnetic material which indicates the ability of magnetic circuit to carry magnetic flux.
μ = B / H
Unit: Henry / meter
Permeability of free space or air or non magnetic material μ0=4*Π*10-7 Henry/m
  Relative permeability, μr : μ/μ0
Analogy: Conductivity

## Slide 11: Magnetic Permeability (μ)
In general, we can write B = μH.
μ is called the permeability of the material.
Normally, we write μ = μr μ0.
μr is called relative permeability (just a number).

## Slide 12: Analogy with Electric circuits
Similarities: |  |  | 
Electric circuit |  | Magnetic circuit | 
Quantity | Unit | Quantity | Unit
EMF (E=IR) | Volt (V) | MMF (F=ɸS) | Ampere-turns
Current (I) | Ampere (A) | Flux (ɸ) | Weber (Wb)
Current density (J) | A/ m2 | Flux density (B) | Wb / m2 or Tesla
Resistance (R) | Ohm (Ω) | Reluctance (S) | Ampere-turns/Wb
Electric field strength (E) | Volts/m | Magnetic field strength (H) | Ampere-turns/m
Conductivity (σ) σ=l/RA | Siemen/m | Permeability, µ µ=l/SA | Henry/m
Magnetic circuit
‘l’ is the length and ‘A ‘is the area of cross section of the conductor

## Slide 13: Differences between electric and magnetic circuits
  In electrical circuit current actually flows.
  In magnetic circuit flux is created, and it is not a flow.
Magnetic circuit

## Slide 14: Example 1
Calculate the magnetomotive force (mmf) required to produce a flux of 0.015 Wb across an air gap of 2.5 mm long, having an effective area of 200 cm2.
Solution :

## Slide 15: Composite Magnetic Circuit
Case 1 :

## Slide 17
Case 2 : (with air gap)
Total reluctance,

## Slide 18
Since the relative permeability μr (= μ1/ μ0) of steel is very large (of the order of thousand), the major contribution in the total reluctance R is by the air-gap, though its length l2 may be quite small (say, a few millimetres).

## Slide 19: Parallel and Series-Parallel Magnetic Circuits

## Slide 20: Thank You