## Slide 1: Lecture 3 Power & Energy

## Slide 2: Power & Energy
Power in an electric circuit
  P = VI = I2R =V2/R
Energy in an electric circuit
  E=P*t = VI*t = I2R*t
Joule’s Law of Heating
  The heat developed in an electrical circuit due to flow of current varies directly as
  the square of the current, E α I2
  the resistance of the circuit, Eα R
  the time of flow, E α t
  E = I2Rt
Practical unit of electrical energy - kWh

## Slide 3: Power & Energy
Q. A 100W light bulb burns on an average of 10 hours a day for one week. The weekly consumption of energy will be
  (a) 7 kWh
  (b) 70 kWh
  (c) 0.7 kWh
  (d) none of the above
Answer
  E= P*t = 100W*(7*10)h = 7000Wh=7kWh=7units
  (a) 7 kWh

## Slide 4: Power & Energy
Q. Four 100W bulbs are connected in parallel across a supply. If one bulb gets fused:
  (a) no bulb will light
  (b) all four bulbs will light
  (c) rest of the 3 bulbs will light
  (d) none of the above [3]
Answer
  (c) rest of the 3 bulbs will light
  the fused circuit becomes open circuited, other 3 circuits remain closed and functional.

## Slide 5: Power & Energy
Q. Four 100W bulbs are connected in series across a supply. If one bulb gets fused:
  (a) no bulb will glow
  (b) all four bulbs will light
  (c) rest of the 3 bulbs will light
  (d) none of the above [3]
Answer
  (a) no bulb will glow
  the entire circuit becomes open circuited

## Slide 6: Power & Energy
Q. A heater takes a current of 8A from a 230V source for 12h. Calculate the energy consumed in kWh.
Answer
  P=V*I = 230*8 = 1840W
  E= P*t = 1840W*(12)h = 22080Wh = 22 kWh = 22 units

## Slide 7: References
[1] Edward Hughes. “Electrical and Electronic Technology”, 10th Edition, Pearson Education Asia, 2011.
[2] William H. Hayt Jr. ,Jack E Kemmerly, Steven M Durbin, “Engineering Circuit Analysis”, 6th Editions, Tata McGraw Hill Publishing Company
[3] Vincent Del Toro, ‘Electrical Engineering Fundamentals’, Second Edition, Prentice Hall of India Private Limited, 2003

## Slide 8: Thank You