## Slide 1: Bipolar Junction Transistor

## Slide 2: Fundamentals of Transistor
Lecture 32
?
?
?

## Slide 3: Structure of Transistor
Terminals of a BJT
Emitter
Base
Collector
What is biasing?
Setting an initial working condition for the transistor to function by applying a fixed voltage.
Lecture 32

## Slide 4: On biasing a transistor
The current will flow through different parts of the BJT
Job of emitter, base, and collector
Lecture 32

## Slide 5: Transistor parameters
Most electron from emitter reaches collector
Less than 1% fail to reach collector
Basic current equation of BJT is IE=IB+IC , where IB<<IC, IE=IC
Alpha and beta current gain
Lecture 32
(a) Conventional flow; (b) electron flow; (c) pnp currents
200 to 300 for low power and
20 to 100 for high power

## Slide 6: Problems
A transistor has a current gain of 150 and a base current of 30 µA. What is the collector current?
Solution
with IC = βdc * IB, IC= 150*30µ = 4500µA = 4.5mA
The collector current is 10 mA, and the base current is 0.1 mA. What is the alpha dc?
solution
Total current IE=10+0.1=10.1A
αdc= 10/10.1 = 0.9901
Lecture 32

## Slide 7: Subscript terminology
The voltage reffered in the circuit of a BJT has 2 forms
Vyy, Vzz, Vyx, and Vzx
When the subscript are the same, they refer to the voltage applied
When the subscript are different, they refer to the voltage developed across the diodes of the transistor
Third form of terminology which is used in analysis – VC , VB , and VE , they represent the terminal voltage of the transistor
VCE = VC - VE
VCB = VC - VB
VBE = VB - VE
Lecture 32

## Slide 8: Characteristics curve
Lecture 32
Base curve
Collector curve

## Slide 9: Few terms to know
Lecture 32
Saturation region
Active region
Breakdown region
Cutoff region

## Slide 10: Problems
A transistor circuit has a collector supply voltage of 20 V, a collector resistance of 1.5 kΩ, and a collector current of 6 mA. What is the collector-emitter voltage?
Solution
VCC=20V, RC=1.5kΩ, IC=6mA
VCC = ICRC+VCE
So; 20 = 1.5*10^3*6*10^-3 + VCE
Therefore; VCE = 11V

## Slide 11: Reference
A. P. Malvino, “Electronic Principles”, 7th Edition, Tata McGraw Hill, 2007.
David A. Bell, “Electronic Devices and Circuits”, 5th Edition, Oxford University Press, 2008.
4. Michael Tooley B. A., “Electronic circuits: Fundamentals and Applications”, 3rd Edition, Elsevier Limited, 2006.

## Slide 12: Thank You