## Slide 1: Lecture 8 Voltage and current division rule

## Slide 2: Connection of elements!!
Resistance in series.
    Voltage division rule.
Resistance in parallel.
    Current division rule.

## Slide 3: Series resistance and Voltage division
V1= iR1 and V2= iR2  (eq 1)
V-V1-V2=0  (eq2)
V-iR1-iR2=0  (eq3)
V=i(R1+R2)
i=V/(R1+R2) (eq4)
V1=V*R1/(R1+R2)
V2=V*R2/(R1+R2)
Let V1,V2 be the voltages
Across R1 and R2 respectively.

## Slide 4: Parallel resistance and Current division
V= i1R1 and V= i2R2
i1=V/R1 and i2=V/R2 (eq1)
i= i1+i2
= V/R1 + V/R2
= V ( 1/R1 + 1/R2)
= V/Req
V= i. Req (eq2)
i1=i*R2/(R1+R2)
i2=i*R1/(R1+R2)
Let i1,i2 be the current
through R1 and R2 respectively.
i1= V/R1= i. Req/ R1
=i(R1R2)/(R1+R2)
=iR2/(R1+R2)

## Slide 5: Exercise 1. Find current through the branches.
Step 1. Find Req
10 Ω || 40 Ω = 8 Ω
12 Ω ||6 Ω = 4 Ω
Req= 8+4= 12 Ω
i= V/Req
= 10/12
=0.833 A
Current division rule
i1=i*R2/(R1+R2)
i2=i*R1/(R1+R2)

## Slide 6: Continued…
i1= 0.833 * 6/(6+12)
= 0.278 A
i2= 0.833* 12/ (6+12)
=0.553A
Similarly
i3= 0.833*40/(10+40)
=0.66A
i4=0.833*10/(10+40)
=0.166A

## Slide 7: Exercise 2. Calculate VAB for the network.
Applying Voltage division rule.
V1=V*R1/(R1+R2)
V21=V*R2/(R1+R2)
VAC= R3.V/ (R1+R3)
= 15*20/(15+10)
=7.5V
VBC= R4.V/(R2+R4)
=10.20/(40+10)
=4V
Apply KVL in loop ABC
VAB+VBC+VCA=0
VAB+VBC-VAC=0
VAB= VAC- VBC
=7.5-4
=3.5V

## Slide 8
Thank you
Lecture 8